Rubén Comerón Galán

Práctica 4-Sumador RCA

El modelo VHDL del sumador compuesto por semisumadores es:

ENTITY RCA IS
GENERIC (n: INTEGER:=8);
PORT(x_in, y_in: IN BIT_VECTOR(n-1 downto 0); c_in: IN BIT; sal: OUT BIT_VECTOR(n-1 downto 0); c_out: OUT BIT);
END RCA;

ARCHITECTURE estructural OF RCA IS
COMPONENT sumador
PORT (x, y, c_in: IN BIT; s, c_out:OUT BIT);
END COMPONENT;

FOR primero, intermedios, ultimos: sumador USE ENTITY WORK.sumador(estructural);
SIGNAL c_inside: BIT_VECTOR(n-1 downto 0);
BEGIN
G: FOR i IN 0 TO n-1 GENERATE
lsb: IF i = 0 GENERATE
primero: sumador PORT MAP(x_in(0), y_in(0), c_in, sal(0), c_inside(0));
END GENERATE lsb;

siguientes: IF i > 0 AND i < n-1 GENERATE
intermedios: sumador PORT MAP(x_in(i), y_in(i), c_inside(i-1), sal(i), c_inside(i));
END GENERATE siguientes;

msb: IF i = n-1 GENERATE
ultimos: sumador PORT MAP(x_in(i), y_in(i), c_inside(i-1), sal(i), c_out);
END GENERATE msb;
END GENERATE G;
END estructural;

El modelo VHDL del sumador compuesto por suma de productos es:

ENTITY RCA IS
GENERIC (n: INTEGER:=8);
PORT(x_in, y_in: IN BIT_VECTOR(n-1 downto 0); c_in: IN BIT; sal: OUT BIT_VECTOR(n-1 downto 0); c_out: OUT BIT);
END ENTITY;

ARCHITECTURE estructural OF RCA IS
COMPONENT sumador
PORT (x, y, c_in: IN BIT; s, c_out:OUT BIT);
END COMPONENT;
COMPONENT and3
PORT (e1, e2, e3: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT or4
PORT (e1, e2, e3, e4: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT not2
PORT (e: IN BIT; sal: OUT BIT);
END COMPONENT;
SIGNAL c_aux: BIT_VECTOR(n-1 downto 0);
BEGIN
G: FOR i IN 0 TO n-1 GENERATE
lsb: IF i = 0 GENERATE
primeros: sumador PORT MAP(x_in(0), y_in(0), c_in, sal(0), c_aux(0));
END GENERATE lsb;

siguientes: IF i > 0 AND i < n-1 GENERATE
intermedios: sumador PORT MAP(x_in(i), y_in(i), c_aux(i-1), sal(i), c_aux(i));
END GENERATE siguientes;

msb: IF i = n-1 GENERATE
primeros: sumador PORT MAP(x_in(i), y_in(i), c_aux(i-1), sal(i), c_out);
END GENERATE msb;
END GENERATE G;
END estructural;

EL test-bench utilizado para ambos sumadores es:

ENTITY tb_RCA IS
END tb_RCA;

ARCHITECTURE estructural OF tb_RCA IS
COMPONENT RCA
GENERIC (n: INTEGER:=8);
PORT(x_in, y_in: IN BIT_VECTOR(n-1 downto 0);
    c_in: IN BIT;
    sal: OUT BIT_VECTOR(n-1 downto 0);
    c_out: OUT BIT);
END COMPONENT;

FOR componente: RCA USE ENTITY WORK.RCA(estructural);

CONSTANT TAMANO_PALABRA: integer := 2;

SIGNAL a, b, r: BIT_VECTOR(TAMANO_PALABRA-1 downto 0);
SIGNAL cin, cout, marca: BIT;

BEGIN

componente: RCA GENERIC MAP (TAMANO_PALABRA) PORT MAP (A, B, Cin, R, Cout);

PROCESS
VARIABLE valor, i, j, n: INTEGER;
BEGIN

valor:=0;
i:=0;
j:=0;
n:=0;
A<=(others=>'0');
B<=(others=>'0');
Cin<='0';
marca<='0';
WAIT FOR TAMANO_PALABRA*10 ns;
A<=(others=>'1');
Cin<='1';
marca<='1';
WAIT UNTIL Cout='1' AND R(TAMANO_PALABRA-1)='0';
marca<='0';

FOR k IN A'RANGE LOOP
IF A(k)='1' THEN
i:=i+2**k;
END IF;
END LOOP;
FOR k IN B'RANGE LOOP
IF B(k)='1' THEN
j:=j+2**k;
END IF;
END LOOP;
IF Cin='1' THEN
valor:=valor+1;
n:=1;
ELSE
n:=0;
END IF;
FOR k IN R'RANGE LOOP
IF R(k)='1' THEN
valor:=valor+2**k;
END IF;
END LOOP;

IF Cout='1' THEN
valor:=valor+2**TAMANO_PALABRA;
END IF;

ASSERT valor=i+j REPORT "resultado incorrecto" SEVERITY ERROR;
WAIT FOR 2 ns;
WAIT;

END PROCESS;
END estructural;

	Semisumadores	Suma de productos
RTL	11rRTL	9rRTL
ECL	5rECL	5rECL
TTL	11rTTL	9rTTL
CMOS	10rCMOS	9rCMOS