Rubén Comerón Galán

Práctica 5-Sumador CSLA

El modelo VHDL del bloque mencionado en el enunciado de la sesión es:

ENTITY CSL IS
GENERIC (k: INTEGER:=4);
PORT(x_in, y_in: IN BIT_VECTOR(k-1 downto 0); c_in: IN BIT; sal: OUT BIT_VECTOR(k-1 downto 0); c_out: OUT BIT);
END ENTITY;

ARCHITECTURE estructural OF CSL IS

COMPONENT RCA
GENERIC (c: INTEGER:=4);
PORT(x_in, y_in: IN BIT_VECTOR(c-1 downto 0); c_in: IN BIT; sal: OUT BIT_VECTOR(c-1 downto 0); c_out: OUT BIT);
END COMPONENT;
COMPONENT mux21
PORT (e1, e2, control: IN BIT; s: OUT BIT);
END COMPONENT;
COMPONENT and2
GENERIC (retardo: TIME:= 1 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT or2
GENERIC (retardo: TIME:= 1 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
SIGNAL RCA_0, RCA_1: BIT_VECTOR(k-1 DOWNTO 0);
SIGNAL RCA_0_Cout, RCA_1_Cout, Cin_and_Cout: BIT;
BEGIN

RCA_carry_0: RCA PORT MAP(x_in, y_in, '0', RCA_0, RCA_0_Cout);
RCA_carry_1: RCA PORT MAP(x_in, y_in, '1', RCA_1, RCA_1_Cout);
G: FOR i IN 0 TO k-1 GENERATE
multiplexor: mux21 PORT MAP(RCA_0(i), RCA_1(i), c_in, sal(i));
END GENERATE G;
Cout_and: and2 PORT MAP (c_in, RCA_1_Cout, Cin_and_Cout);
Cout_or: or2 PORT MAP (RCA_0_Cout, Cin_and_Cout, c_out);

END estructural;

El modelo VHDL del selector de acarreo (CSLA) es:

ENTITY CSLA IS
GENERIC (n: INTEGER:=16);
PORT(x_in, y_in: IN BIT_VECTOR(n-1 downto 0); c_in: IN BIT; sal: OUT BIT_VECTOR(n-1 downto 0); c_out: OUT BIT);
END ENTITY;

ARCHITECTURE estructural OF CSLA IS

COMPONENT CSL
GENERIC (k: INTEGER:=4);
PORT(x_in, y_in: IN BIT_VECTOR(k-1 downto 0); c_in: IN BIT; sal: OUT BIT_VECTOR(k-1 downto 0); c_out: OUT BIT);
END COMPONENT;
SIGNAL Cout_aux: BIT_VECTOR(3 DOWNTO 0);
CONSTANT k: INTEGER:=4;
BEGIN

G: FOR i IN 0 TO (n/4)-1 GENERATE
lsb: IF i = 0 GENERATE
primero: CSL PORT MAP(x_in((i+1)*k-1 DOWNTO i*k), y_in((i+1)*k-1 DOWNTO i*k), c_in, sal((i+1)*k-1 DOWNTO i*k), Cout_aux(i));
END GENERATE lsb;

siguientes: IF i > 0 AND i < (n/4)-1 GENERATE
intermedios: CSL PORT MAP(x_in((i+1)*k-1 DOWNTO i*k), y_in((i+1)*k-1 DOWNTO i*k), Cout_aux(i-1), sal((i+1)*k-1 DOWNTO i*k), Cout_aux(i));
END GENERATE siguientes;

msb: IF i = (n/4)-1 GENERATE
ultimos: CSL PORT MAP(x_in((i+1)*k-1 DOWNTO (i*k)), y_in((i+1)*k-1 DOWNTO i*k), Cout_aux(i-1), sal((i+1)*k-1 DOWNTO i*k), c_out);
END GENERATE msb;
END GENERATE G;

END estructural;

El test-bench utilizado es:

ENTITY tb_CSLA IS
END tb_CSLA;

ARCHITECTURE estructural OF tb_CSLA IS
COMPONENT CSLA
GENERIC (n: INTEGER:=4; k: INTEGER:=2);
PORT(x_in, y_in: IN BIT_VECTOR(n-1 downto 0);
    c_in: IN BIT;
    sal: OUT BIT_VECTOR(n-1 downto 0);
    c_out: OUT BIT);
END COMPONENT;

FOR componente: CSLA USE ENTITY WORK.CSLA(estructural);

CONSTANT TAMANO_PALABRA: INTEGER := 4;
CONSTANT TAMANO_PALABRA_RCA: INTEGER := 2;

SIGNAL A, B, R: BIT_VECTOR(TAMANO_PALABRA-1 downto 0);
SIGNAL cin, cout, marca: BIT;

BEGIN

componente: CSLA GENERIC MAP (TAMANO_PALABRA) PORT MAP (A, B, Cin, R, Cout);

PROCESS
VARIABLE valor, limite, cuenta_carry, sol: INTEGER;
BEGIN

limite:= 2**TAMANO_PALABRA-1;

FOR i IN 0 TO limite LOOP
valor:=i;

FOR k IN B'REVERSE_RANGE LOOP
A(k)<=BIT'VAL(valor REM 2);--cambiamos A
valor:=valor/2;
END LOOP;

FOR j IN 0 TO limite LOOP
valor:=j;

FOR k IN B'REVERSE_RANGE LOOP
B(k)<=BIT'VAL(valor REM 2);--cambiamos B
valor:=valor/2;
END LOOP;
FOR carry IN 0 TO 1 LOOP
cin<=BIT'VAL(carry REM 2);
WAIT FOR 20 ns;
END LOOP;
END LOOP;
END LOOP;
WAIT;
END PROCESS;
END estructural;