Rubén Comerón Galán

Sesión 6 – Sumador CSK

El código del bloque propagador es:

ENTITY Bloque_P IS
GENERIC (c: INTEGER:=4);
PORT(x_in, y_in: IN BIT_VECTOR(c-1 downto 0); P: OUT BIT);
END ENTITY;

ARCHITECTURE estructural OF Bloque_P IS

COMPONENT and2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;

COMPONENT xor2 IS
GENERIC (retardo: TIME:= 3 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;

SIGNAL xor_0, xor_1, xor_2, xor_3, and_1, and_2: BIT;

BEGIN

bit_0: xor2 PORT MAP(x_in(0), y_in(0), xor_0);
bit_1: xor2 PORT MAP(x_in(1), y_in(1), xor_1);
bit_2: xor2 PORT MAP(x_in(2), y_in(2), xor_2);
bit_3: xor2 PORT MAP(x_in(3), y_in(3), xor_3);
primer_and: and2 PORT MAP(xor_0, xor_1, and_1);
segundo_and: and2 PORT MAP(xor_2, xor_3, and_2);
tercer_and: and2 PORT MAP(and_1, and_2, P);

END ARCHITECTURE;

El código del bloque CSK es:

ENTITY Bloque_CSK IS
GENERIC (c: INTEGER:=4);
PORT(x_in, y_in: IN BIT_VECTOR(c-1 downto 0); c_in: IN BIT; sal: OUT BIT_VECTOR(c-1 downto 0); c_out: OUT BIT);
END ENTITY;

ARCHITECTURE estructural OF Bloque_CSK IS

COMPONENT RCA IS
GENERIC (c: INTEGER:=4);
PORT(x_in, y_in: IN BIT_VECTOR(c-1 downto 0); c_in: IN BIT; sal: OUT BIT_VECTOR(c-1 downto 0); c_out: OUT BIT);
END COMPONENT;
COMPONENT Bloque_P IS
GENERIC (c: INTEGER:=4);
PORT(x_in, y_in: IN BIT_VECTOR(c-1 downto 0); P: OUT BIT);
END COMPONENT;
COMPONENT and2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT or2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
SIGNAL P, c_out_aux, and_aux: BIT;
BEGIN

sumador: RCA PORT MAP(x_in, y_in, c_in, sal, c_out_aux);
propagacion: Bloque_P PORT MAP(x_in, y_in, P);
and_cout: and2 PORT MAP(P, c_in, and_aux);
or_cout: or2 PORT MAP(and_aux, c_out_aux, c_out);

END estructural;

El código del sumador CSK es:

ENTITY CSK IS
GENERIC (n: INTEGER:=16);
PORT(x_in, y_in: IN BIT_VECTOR(n-1 downto 0); c_in: IN BIT; sal: OUT BIT_VECTOR(n-1 downto 0); c_out: OUT BIT);
END ENTITY;

ARCHITECTURE estructural OF CSK IS

COMPONENT Bloque_CSK
GENERIC (c: INTEGER:=4);
PORT(x_in, y_in: IN BIT_VECTOR(c-1 downto 0); c_in: IN BIT; sal: OUT BIT_VECTOR(c-1 downto 0); c_out: OUT BIT);
END COMPONENT;
COMPONENT RCA
GENERIC (c: INTEGER:=4);
PORT(x_in, y_in: IN BIT_VECTOR(c-1 downto 0); c_in: IN BIT; sal: OUT BIT_VECTOR(c-1 downto 0); c_out: OUT BIT);
END COMPONENT;

CONSTANT c: integer:=4;
SIGNAL c_aux: BIT_VECTOR ((n/4)-1 DOWNTO 0);

BEGIN

primeros_bits: RCA PORT MAP(x_in(3 DOWNTO 0), y_in(3 DOWNTO 0), c_in, sal(3 DOWNTO 0), c_aux(0));
G: FOR i IN 1 TO (n/4)-1 GENERATE
siguientes: IF i < (n/4)-1 GENERATE
intermedios: Bloque_CSK PORT MAP(x_in((i+1)*c-1 DOWNTO i*c), y_in((i+1)*c-1 DOWNTO i*c), c_aux(i-1), sal((i+1)*c-1 DOWNTO i*c), c_aux(i));
END GENERATE siguientes;
msb: IF i = c-1 GENERATE
ultimos: Bloque_CSK PORT MAP(x_in((i+1)*c-1 DOWNTO i*c), y_in((i+1)*c-1 DOWNTO i*c), c_aux(i-1), sal((i+1)*c-1 DOWNTO i*c), c_out);
END GENERATE msb;
END GENERATE G;
END estructural;

El test-bench para el sumador CSK es:

FOR componente: CSK USE ENTITY WORK.CSK(estructural);

CONSTANT TAMANO_PALABRA: integer := 4;
CONSTANT TAMANO_PALABRA_RCA: INTEGER := 2;

SIGNAL a, b, r: BIT_VECTOR(TAMANO_PALABRA-1 downto 0);
SIGNAL cin, cout, marca: BIT;

BEGIN

componente: CSK GENERIC MAP (TAMANO_PALABRA) PORT MAP (A, B, Cin, R, Cout);

PROCESS
VARIABLE valor, limite, cuenta_carry, sol: INTEGER;
BEGIN

limite:= 2**TAMANO_PALABRA-1;

FOR i IN 0 TO limite LOOP
valor:=i;

FOR k IN B'REVERSE_RANGE LOOP
A(k)<=BIT'VAL(valor REM 2);--cambiamos A
valor:=valor/2;
END LOOP;

FOR j IN 0 TO limite LOOP
valor:=j;

FOR k IN B'REVERSE_RANGE LOOP
B(k)<=BIT'VAL(valor REM 2);--cambiamos B
valor:=valor/2;
END LOOP;
FOR carry IN 0 TO 1 LOOP
cin<=BIT'VAL(carry REM 2);
WAIT FOR 30 ns;
END LOOP;
END LOOP;
END LOOP;
WAIT;
END PROCESS;
END estructural;