Rubén Comerón Galán

Sesión 7-NEG-C2

Activo a partir del primer ‘1’:

Bloque negador:

ENTITY Bloque_neg IS
PORT(x, e, c_in: IN BIT; r, c_out: OUT BIT);
END ENTITY;

ARCHITECTURE estructural OF Bloque_neg IS

COMPONENT and2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT or2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT xor2 IS
GENERIC (retardo: TIME:= 3 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;

SIGNAL e_and_c: BIT;

BEGIN

c_and_e: and2 PORT MAP(e, c_in, e_and_c);
salida: xor2 PORT MAP(x, e_and_c, r);
siguiente_c: or2 PORT MAP(x, c_in, c_out);

END estructural;

Negador:

ENTITY NEG_C2 IS
GENERIC(n:INTEGER :=16);
PORT(x, e: IN BIT_VECTOR(n-1 DOWNTO 0); r: OUT BIT_VECTOR(n-1 DOWNTO 0); des: OUT BIT);
END ENTITY;

ARCHITECTURE estructural OF NEG_C2 IS

COMPONENT Bloque_neg IS
PORT(x, e, c_in: IN BIT; r, c_out: OUT BIT);
END COMPONENT;
COMPONENT not2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT and2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
SIGNAL c: BIT_VECTOR(n-1 DOWNTO 0);
SIGNAL d: BIT;

BEGIN

G: FOR i IN 0 TO n-1 GENERATE
primero: IF i = 0 GENERATE
primer_bit: Bloque_neg PORT MAP(x(i), e(i), x(i), r(i), c(i));
END GENERATE primero;
intermedios: IF i > 0 GENERATE
siguientes: Bloque_neg PORT MAP(x(i), e(i), c(i-1), r(i), c(i));
END GENERATE intermedios;
END GENERATE G;
desbor: not2 PORT MAP(c(n-2), d)
desbordamiento: and2 PORT MAP(x(n-1), d, des);

END estructural;

A partir del primer ‘0’:

Bloque negador:

ENTITY Bloque_neg IS
PORT(x, e, c_in: IN BIT; r, c_out: OUT BIT);
END ENTITY;

ARCHITECTURE estructural OF Bloque_neg IS

COMPONENT and2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT or2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT xor2 IS
GENERIC (retardo: TIME:= 3 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT not2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e: IN BIT; sal: OUT BIT);
END COMPONENT;

SIGNAL e_and_c, x_negada: BIT;

BEGIN

neg_x: not2 PORT MAP(x, x_negada);
c_and_e: and2 PORT MAP(e, c_in, e_and_c);
salida: xor2 PORT MAP(x, e_and_c, r);
siguiente_c: or2 PORT MAP(x_negada, c_in, c_out);

END estructural;

Negador:

ENTITY NEG_C2 IS
GENERIC(n:INTEGER :=16);
PORT(x, e: IN BIT_VECTOR(n-1 DOWNTO 0); r: OUT BIT_VECTOR(n-1 DOWNTO 0); des: OUT BIT);
END ENTITY;

ARCHITECTURE estructural OF NEG_C2 IS

COMPONENT Bloque_neg IS
PORT(x, e, c_in: IN BIT; r, c_out: OUT BIT);
END COMPONENT;
COMPONENT not2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT or2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
SIGNAL c, cal_d: BIT_VECTOR(n-1 DOWNTO 0);
SIGNAL d, de, x_neg_0: BIT;

BEGIN

x_neg: not2 PORT MAP(x(0), x_neg_0);
G: FOR i IN 0 TO n-1 GENERATE
primero: IF i = 0 GENERATE
primer_bit: Bloque_neg PORT MAP(x(i), e(i), x_neg_0, r(i), c(i));
END GENERATE primero;
intermedios: IF i > 0 GENERATE
siguientes: Bloque_neg PORT MAP(x(i), e(i), c(i-1), r(i), c(i));
END GENERATE intermedios;
END GENERATE G;
B: FOR i IN 1 TO n-2 GENERATE
primer: IF i = 1 GENERATE
primeros_bit: or2 PORT MAP(x(i), x(i-1), cal_d(i));
END GENERATE primer;
intermedio: IF i > 1 AND i < n-2 GENERATE
siguiente: or2 PORT MAP(x(i), cal_d(i-1), cal_d(i));
END GENERATE intermedio;
final: IF i = n-2 GENERATE
ultimo: or2 PORT MAP(x(i), cal_d(i-1), cal_d(i));
END GENERATE final;
END GENERATE B;
d_negada: not2 PORT MAP(x(n-1), d);
desborde: or2 PORT MAP(d, cal_d(n-2), de);
desbor: not2 PORT MAP(de, des);

END estructural;

Hasta primer ‘1’:

Bloque negador:

ENTITY Bloque_neg IS
PORT(x, e, c_in: IN BIT; r, c_out: OUT BIT);
END ENTITY;

ARCHITECTURE estructural OF Bloque_neg IS

COMPONENT and2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT or2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT xor2 IS
GENERIC (retardo: TIME:= 3 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT not2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e: IN BIT; sal: OUT BIT);
END COMPONENT;

SIGNAL e_and_c, x_negada: BIT;

BEGIN

neg_x: not2 PORT MAP(x, x_negada);
c_and_e: and2 PORT MAP(e, c_in, e_and_c);
salida: xor2 PORT MAP(x, e_and_c, r);
siguiente_c: and2 PORT MAP(x_negada, c_in, c_out);

END estructural;

Negador:

ENTITY NEG_C2 IS
GENERIC(n:INTEGER :=16);
PORT(x, e: IN BIT_VECTOR(n-1 DOWNTO 0); r: OUT BIT_VECTOR(n-1 DOWNTO 0); des: OUT BIT);
END ENTITY;

ARCHITECTURE estructural OF NEG_C2 IS

COMPONENT Bloque_neg IS
PORT(x, e, c_in: IN BIT; r, c_out: OUT BIT);
END COMPONENT;
COMPONENT and2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT not2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT or2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
SIGNAL c: BIT_VECTOR(n-1 DOWNTO 0);
SIGNAL x_neg_0: BIT;

BEGIN

x_neg: not2 PORT MAP(x(0), x_neg_0);
G: FOR i IN 0 TO n-1 GENERATE
primero: IF i = 0 GENERATE
primer_bit: Bloque_neg PORT MAP(x(i), e(i), x_neg_0, r(i), c(i));
END GENERATE primero;
intermedios: IF i > 0 GENERATE
siguientes: Bloque_neg PORT MAP(x(i), e(i), c(i-1), r(i), c(i));
END GENERATE intermedios;
END GENERATE G;
desborde: and2 PORT MAP(x(n-1), c(n-2), des);

END estructural;

Hasta primer ‘0’:

Bloque negador:

ENTITY Bloque_neg IS
PORT(x, e, c_in: IN BIT; r, c_out: OUT BIT);
END ENTITY;

ARCHITECTURE estructural OF Bloque_neg IS

COMPONENT and2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT or2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT xor2 IS
GENERIC (retardo: TIME:= 3 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;

SIGNAL e_and_c: BIT;

BEGIN

c_and_e: and2 PORT MAP(e, c_in, e_and_c);
salida: xor2 PORT MAP(x, e_and_c, r);
siguiente_c: and2 PORT MAP(x, c_in, c_out);

END estructural;

Negador:

ENTITY NEG_C2 IS
GENERIC(n:INTEGER :=16);
PORT(x, e: IN BIT_VECTOR(n-1 DOWNTO 0); r: OUT BIT_VECTOR(n-1 DOWNTO 0); des: OUT BIT);
END ENTITY;

ARCHITECTURE estructural OF NEG_C2 IS

COMPONENT Bloque_neg IS
PORT(x, e, c_in: IN BIT; r, c_out: OUT BIT);
END COMPONENT;
COMPONENT not2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT or2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT and2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
SIGNAL c, cal_d: BIT_VECTOR(n-1 DOWNTO 0);
SIGNAL x_neg_c: BIT;

BEGIN

G: FOR i IN 0 TO n-1 GENERATE
primero: IF i = 0 GENERATE
primer_bit: Bloque_neg PORT MAP(x(i), e(i), x(i), r(i), c(i));
END GENERATE primero;
intermedios: IF i > 0 GENERATE
siguientes: Bloque_neg PORT MAP(x(i), e(i), c(i-1), r(i), c(i));
END GENERATE intermedios;
END GENERATE G;
B: FOR i IN 1 TO n-2 GENERATE
primer: IF i = 1 GENERATE
primeros_bit: or2 PORT MAP(x(i), x(i-1), cal_d(i));
END GENERATE primer;
intermedio: IF i > 1 AND i < n-2 GENERATE
siguiente: or2 PORT MAP(x(i), cal_d(i-1), cal_d(i));
END GENERATE intermedio;
final: IF i = n-2 GENERATE
ultimo: or2 PORT MAP(x(i), cal_d(i-1), cal_d(i));
END GENERATE final;
END GENERATE B;
neg_x_c: not2 PORT MAP(cal_d(n-2), x_neg_c);
desbordamiento: and2 PORT MAP(x_neg_c, x(n-1), des);

END estructural;

El test-bench es:

ENTITY tb_NEG_C2 IS
END tb_NEG_C2;

ARCHITECTURE estructural OF tb_NEG_C2 IS
COMPONENT NEG_C2 IS
GENERIC (n: INTEGER:=4);
PORT(x, e: IN BIT_VECTOR(n-1 downto 0);
    r: OUT BIT_VECTOR(n-1 downto 0);
    des: OUT BIT);
END COMPONENT;

FOR componente: NEG_C2 USE ENTITY WORK.NEG_C2(estructural);

CONSTANT TAMANO_PALABRA: integer := 4;

SIGNAL a, b, r: BIT_VECTOR(TAMANO_PALABRA-1 downto 0);
SIGNAL marca, d: BIT;

BEGIN

componente: NEG_C2 GENERIC MAP (TAMANO_PALABRA) PORT MAP (A, B, R, D);

PROCESS
VARIABLE valor, limite, cuenta_carry, sol: INTEGER;
BEGIN

limite:= 2**TAMANO_PALABRA-1;

FOR i IN 0 TO limite LOOP
valor:=i;

FOR k IN B'REVERSE_RANGE LOOP
A(k)<=BIT'VAL(valor REM 2);--cambiamos A
valor:=valor/2;
END LOOP;

FOR j IN 0 TO limite LOOP
valor:=j;

FOR k IN B'REVERSE_RANGE LOOP
B(k)<=BIT'VAL(valor REM 2);--cambiamos B
valor:=valor/2;
END LOOP;
WAIT FOR 20 ns;
END LOOP;
END LOOP;
WAIT;
END PROCESS;
END estructural;