Rubén Comerón Galán

Sesión 8 Sumador-restador

El código para el sumador restador es:

ENTITY SUMADOR_RESTADOR IS
GENERIC(c: INTEGER:=4);
PORT(X, Y: IN BIT_VECTOR(c-1 DOWNTO 0); SUMA_RESTA: IN BIT; R: OUT BIT_VECTOR(c-1 DOWNTO 0); AC, DES, SIG, CERO: OUT BIT);
END SUMADOR_RESTADOR;

ARCHITECTURE estructural OF SUMADOR_RESTADOR IS
COMPONENT RCA IS
GENERIC (c: INTEGER:=2);
PORT(x_in, y_in: IN BIT_VECTOR(c-1 downto 0); c_in: IN BIT; sal, c_out: OUT BIT_VECTOR(c-1 downto 0));
END COMPONENT;
COMPONENT NEG_C2 IS
GENERIC(n:INTEGER :=4);
PORT(x: IN BIT_VECTOR(n-1 DOWNTO 0); e: IN BIT; r: OUT BIT_VECTOR(n-1 DOWNTO 0); des: OUT BIT);
END COMPONENT;
COMPONENT or2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT xor2 IS
GENERIC (retardo: TIME:= 3 ns);
PORT (e1, e2: IN BIT; sal: OUT BIT);
END COMPONENT;
COMPONENT not2 IS
GENERIC (retardo: TIME:= 1 ns);
PORT (e: IN BIT; sal: OUT BIT);
END COMPONENT;

FOR ALL: RCA USE ENTITY WORK.RCA(estructural);
FOR ALL: NEG_C2 USE ENTITY WORK.NEG_C2(estructural);
FOR ALL: or2 USE ENTITY WORK.or2(estructural);
FOR ALL: xor2 USE ENTITY WORK.xor2(comportamiento);
FOR ALL: not2 USE ENTITY WORK.not2(comportamiento);

CONSTANT TAMANO_PALABRA: INTEGER:=4;
SIGNAL Y_SIGNED, R_aux, C_out, det_0: BIT_VECTOR(c-1 DOWNTO 0);
SIGNAL Des_cambio_signo: BIT;
BEGIN
negador: NEG_C2 PORT MAP(Y, SUMA_RESTA, Y_SIGNED, Des_cambio_signo);
componente: RCA PORT MAP(X, Y_SIGNED, SUMA_RESTA, R_aux, C_out);
G: FOR I IN 0 TO TAMANO_PALABRA-2 GENERATE
primero: IF I=0 GENERATE
detector_0: or2 PORT MAP(R_aux(i), R_aux(i+1), det_0(i));
END GENERATE;
siguientes: IF I>0 AND I<TAMANO_PALABRA-1 GENERATE
detect_0: or2 PORT MAP(det_0(i-1), R_aux(i+1), det_0(i));
END GENERATE;
END GENERATE;
deteccion_0: not2 PORT MAP(det_0(TAMANO_PALABRA-2), CERO);
SIG<=R_aux(TAMANO_PALABRA-1);
desbordamiento: xor2 PORT MAP(C_out(TAMANO_PALABRA-1), C_out(TAMANO_PALABRA-2), DES);
acarreo: xor2 PORT MAP(SUMA_RESTA, C_out(TAMANO_PALABRA-1), AC);

END ARCHITECTURE;

El código para su test-bench es:

ENTITY tb_sumador_restador IS
END tb_sumador_restador;

ARCHITECTURE estructural OF tb_sumador_restador IS
COMPONENT SUMADOR_RESTADOR IS
GENERIC(c: INTEGER:=4);
PORT(X, Y: IN BIT_VECTOR(c-1 DOWNTO 0); SUMA_RESTA: IN BIT; R: OUT BIT_VECTOR(c-1 DOWNTO 0); AC, DES, SIG, CERO: OUT BIT);
END COMPONENT;

FOR componente: sumador_restador USE ENTITY WORK.sumador_restador(estructural);

CONSTANT TAMANO_PALABRA: INTEGER := 4;
CONSTANT TAMANO_PALABRA_RCA: INTEGER := 2;

SIGNAL A, B, R: BIT_VECTOR(TAMANO_PALABRA-1 downto 0);
SIGNAL sum_sub, ac, des, sig, cero: BIT;

BEGIN

componente: sumador_restador GENERIC MAP (TAMANO_PALABRA) PORT MAP (A, B, sum_sub, R, ac, des, sig, cero);

PROCESS
VARIABLE valor, limite, cuenta_carry, sol: INTEGER;
BEGIN

limite:= 2**TAMANO_PALABRA-1;

FOR i IN 0 TO limite LOOP
valor:=i;

FOR k IN B'REVERSE_RANGE LOOP
A(k)<=BIT'VAL(valor REM 2);--cambiamos A
valor:=valor/2;
END LOOP;

FOR j IN 0 TO limite LOOP
valor:=j;

FOR k IN B'REVERSE_RANGE LOOP
B(k)<=BIT'VAL(valor REM 2);--cambiamos B
valor:=valor/2;
END LOOP;
FOR carry IN 0 TO 1 LOOP
sum_sub<=BIT'VAL(carry REM 2);
WAIT FOR 20 ns;
END LOOP;
END LOOP;
END LOOP;
WAIT;
END PROCESS;
END estructural;